## Slide 1: Harmonic Input
ME 357

## Slide 2: Objectives
By the end of this section, you should be able to
Read log-scale plot
Use Bode plot to determine magnitude and phase of output signal
Find closed-form steady-state outputs for linear systems with simple harmonic input
Use normalized Bode plot to design systems to operate away from resonance
Understand sensor dynamic range from their Bode plot
Design simple analog LP and HP filters

## Slide 3: Frequency Domain
In time domain, we have looked at only step input
  In this section, we look at harmonic inputs with constant angular frequency
At steady state, output can be attenuated () or amplified () and have phase shift (right or left), but will have same frequency as input function
and are dependent on input frequency
We will not calculate transient behavior in this course
G(s)
(Linear)
Notes: This is true for linear systems at steady-state
Same with cosine

## Slide 4: Finding Parameters
If we do not know TF, can run experiment and sweep though input frequencies and measure and at each
If we know TF then
Notes: We will not look at experimental data in this course

## Slide 5: Analytic Example

## Slide 6: Analytic Example

## Slide 7: Phase
Phase lead (positive value) or phase lag (negative value) is what fraction of forcing cycle output is offset from input
Examples
  When phase is 0⁰, output cycle matches input cycle (in-phase)
  When phase is -120⁰, output lags input by a third of a cycle
  When phase is -180⁰, output lags half cycle behind input (antiphase)

## Slide 8: Bode Diagram
Bode diagram visualizes magnitude and phase shift over range of input frequencies
Matlab plots as log-log and semi-log plots
  y-axis in decibels (for amplitude) and degrees (for phase)
  x-axis (frequency) in log scale
Spike in amplification indicates resonance or instability at that input frequency(ies)
  Usually do not want to operate near spike
  May change either input frequency or system parameters to move away from spike
Notes: it is a plot using the previous definitions of magnitude and phase

## Slide 9: Example 1
Find analytic steady-state output for TF
using inputs of
use Bode diagram to analyze and Simulink to simulate.

## Slide 10: Example 1 Bode Diagram
Notes: This matches what we found analytically

## Slide 11: Example 1 Simulink Model

## Slide 12: Example 1 Simulation
Input of
Magnitude of
Phase shift of -45° (output lags input by 1/8 cycle)

## Slide 13: Example 1 Simulation
Input of
Magnitude of
Phase shift of ~-90° (output lags input by about a quarter cycle)

## Slide 14: 2nd-Order (and Higher) Systems
2nd-Order Systems have amplitude spike in Bode Diagram at resonant frequency when
  No magnitude spike when overdamped or “highly” damped:
Forcing at or near resonant frequency should generally be avoided to prevent resonance
  Can change forcing frequency
  Can change system parameters
    Changing spring constant or mass will shift natural/resonant frequency
    Changing damping will shift resonant frequency and
    Raising damping will lower magnitude of spike
Notes: The resonant frequency is close to the natural frequency (especially for low damping) but always lower

## Slide 15: 2nd-Order (and Higher) Systems
With increasing damping
Spike peak lowers
Spike shifts left

## Slide 16: Rotating Machinery Example 2
For this support
(including )
Assess response of system using Bode diagram.

## Slide 17: FBD Example 2
=
Notes: Accounting for only vertical force of rotating machine

## Slide 18: Example 2
Notes: Very low damping but not zero

## Slide 19: Bode Diagram Example 2
Notes: Damping is very low so wr ~ wn

## Slide 20: Rotating Machinery Example 2
Angular velocity of motor matches natural frequency of platform, causing resonance
Motor runs at specified speed
  As example, can add second identical spring, doubling

## Slide 21: Bode Diagram Example 2

## Slide 22: Transmissibility
Ratio of output force or motion to input force or motion (must be like quantities)

## Slide 23: Vibration Isolator
For rotating machinery, may not want it to transmit force into shared support (e.g., shop floor) as it can disrupt other rotating machines
Can put vibration isolator between machine and support to reduce transferred force

## Slide 24: Relative-Frequency Bode Diagram
Previously used Bode diagram to investigate how different input frequencies would impact amplitude and phase of steady-state output
Can make relative-frequency bode diagram to investigate how ratio of input frequency to natural frequency impacts behavior
  Can use this for 1-DOF systems only (multi-DOF systems have multiple natural frequencies)
  In TF, with denominator in standard form, replace “” with “1”
  Plot Bode diagram of modified TF, horizontal axis is
Useful when we do not know the natural frequency before we need to reference Bode plot

## Slide 25: Example 3
A rotating machine of mass has an unbalanced mass a distance from the center of rotation. (The mass includes mass ). The operating speed is 10 Hz. Suppose that the machine is mounted on an isolator consisting of a spring and damper, as shown. If it is desired that be 0.2, specify the spring constant () and damping coefficient () such that only 10% of the excitation force is transmitted into the foundation. Determine the amplitude of this transmitted force. Verify analysis in simulation.
Notes: Using RF bode plot because we do not have both wn and z beforehand

## Slide 26: FBD Example 3
=
=
Notes: I assume ft is positive up, could assume the opposite with little difference in results
Used Mathematica for the algebra

## Slide 27: Example 3
Notes: 1: in standard form
2: let zeta = 0.2
3: set wn to 1 for RF Bode diagram

## Slide 28: Example 3
Notes: 1: in standard form
2: let zeta = 0.2
3: set wn to 1 for RF Bode diagram

## Slide 29: RF Bode Diagram Example 3
Notes: Fairly low damping so wr~wn

## Slide 30: Example 3
Notes: 1: in standard form
2: let zeta = 0.2
3: set wn to 1 for RF Bode diagram

## Slide 31: Example 3
Notes: 1: in standard form
2: let zeta = 0.2
3: set wn to 1 for RF Bode diagram

## Slide 32: Example 3
Notes: Output should be 10% of input by design

## Slide 33: Simulink Model Example 3

## Slide 34: Simulation Example 3
Transient response

## Slide 35: Example 4 Seismograph
The displacement of mass m relative to inertial space is denoted by x, the displacement of the case relative to inertial space by y. The displacement y is the input to system and, in the case of earthquakes, is approximately sinusoidal, or . An earthquake has a frequency typically in the range of 1-10Hz. In the seismograph, we measure relative displacement between x and y. Choose , and such that the seismograph can measure Y accurately (at steady state).

## Slide 36: Example 4 RF Bode Diagram

## Slide 37: Example 4 RF Bode Diagram

## Slide 38: Example 6
A machine of mass m mounted on a vibration isolator in which spring is the load-carrying spring and viscous damper is in series with spring .
Determine the force transmissibility when the machine is subjected to a sinusoidal excitation force
Let

## Slide 39: Example 6

## Slide 40: Example 6

## Slide 41: Multi-DOF Systems
May have multiple natural frequencies (if 4th-order or higher)
Natural frequencies found by taking magnitudes of eigenvalues of A or poles of TF
Peaks on Bode diagram(s) may be near natural frequencies
May be easier to start in SS and convert to TF

## Slide 42: Multi DOF Systems Example 5
k1 = 20 N/m; k2 = 30 N/m;
b1 = 5 N-s/m
m1 = 10 kg; m2 = 15 kg
Is system stable or unstable?
Find natural frequencies of system
Find exact steady-state response of positions when

## Slide 43: Multi DOF Systems Example 5
A
B
C
D
Notes: Similar to 9.2

## Slide 44: Multi DOF Systems Example 5
Notes: Using ss2tf

## Slide 45: Multi DOF Systems Example 5
Notes: Using ss2tf

## Slide 46: Multi DOF Systems Example 5

## Slide 47: Multi DOF Systems Example 5

## Slide 48: Multi DOF Systems Example 5
Notes: When there is a single input

## Slide 49: Multi DOF Systems Example 5

## Slide 50: Multi DOF Systems Example 5
Transient response

## Slide 51: Multi DOF Systems Example 5

## Slide 52: Sensors & Filters

## Slide 53: Sensors
Convert measurement of one type into voltage reading
  E.g., thermocouple measure temperature, accelerometer measures acceleration, ultrasonic sensor measures position
Sensors themselves are TFs
  Convert input into voltage output
  May be 1st, 2nd or other order
  Can introduce lag and amplification
    Takes time for thermocouple to absorb/dissipate heat
    Accelerometer has to physically vibrate and overcome inertia
Sensors in system give you observables as discussed in SS modeling
    These are quantities we can directly measure in real-time to control system (C matrix)
Notes: Not universally true voltage output but good enough for this class
A matrix described physics of the system, C describes what we can actually measure

## Slide 54: Sensor Range
Ideal sensor
  Sensitive to measured property only
  Does not influence measured property
Calibration
  Need to know how voltage reading corresponds to value of measured quantity
  Take several measurements at known quantities to develop linear relation
Sensors can have dynamic error due to rapid changes in measured property
  Frequency range where magnitude and phase constant on Bode plot minimizes this error
  Operate sensor in this range for known and constant amplification and phase difference with respect to actual signal
Notes: e.g., measure thermocouple in boiling water (100C) and ice water (0C)
e.g. accels. are sensitive to temperature
mass of accel. can change natural freqs. of beam it measures
Would not have to be linear

## Slide 55: Sensor Range Example
For this sensor (e.g. input is force, output is voltage) sensing range is rad/sec. Below this frequency our output magnitude constant (about 8% of the input) and in phase. This sensor is good for low frequency applications.

## Slide 56: Measurement/Sensor Range Example
For this sensor, sensing range is about rad/sec. Within this range output magnitude constant and phase shift is small. This sensor is good for medium frequency applications.

## Slide 57: Filtering
Real signals contain undesirable noise
  Signals not one pure harmonic: contain number of frequencies
  E.g., 60 Hz line noise, loose connections add to signal
If noise occurs at frequencies outside what we want to measure, it can be filtered out
  Typically choose a cutoff frequency (frequency when magnitude is)
  Filter will have rolloff
Types of filters
  Low-pass
  High-pass
  Band-pass
  Notch
May introduce lag into output signal
Notes: How do we know what freqs. we want to measure?

## Slide 58: Passive LP Filter Example
Create simple 1st-order low-pass filter with 5 Hz cutoff
Simulate passing input signal of through filter and observing output
How could this filter be constructed?
Notes: cutoff frequency is reciprocal of time constant in 1st-order

## Slide 59: LP Filter Example Bode Plot
Notes: Note cutoff freq.

## Slide 60: LP Filter Example Output

## Slide 61: LP Filter Example Design
Desired TF
TF of circuit
Pick and such that
Notes: would pick C first as it is more limited in available choices. May not get exact value for cutoff with off-the-shelf parts

## Slide 62: Passive HP Filter Example
Create simple 1st-order high-pass filter with 5 Hz cutoff
Simulate passing input signal of through filter and observing output
How could this filter be constructed?
Notes: cutoff frequency is reciprocal of time constant in 1st-order system

## Slide 63: HP Filter Example Bode Plot
Notes: Note cutoff freq.

## Slide 64: HP Filter Example Output
Notes: High frequency remains

## Slide 65: HP Filter Example Design
Desired TF
TF of circuit
Pick and such that
Notes: would pick C first as it is more limited in available choices. May not get exact value for cutoff with off-the-shelf parts

## Slide 66: Higher-Order Filter Example
Create 2nd-order LP filter with 5 Hz cutoff
Simulate passing input signal of through this filter and the 1st-order version and observing output
Compare also to 3rd-order filter
How could these filters be constructed?
Notes: How can we make the roll-off tighter?
cutoff frequency is reciprocal of time constant in 1st-order system

## Slide 67: Higher-Order Filter
Notes: Attenuates high frequency signals more harshly
Phase lag is introduced more

## Slide 68: Construction
Cascading 1st-order filters
Active filters
  Use op-amp(s) to improve roll off and reduce lag
  Can simplify construction and be adjustable
  Require external power for op-amps
https://www.electronics-tutorials.ws/filter/filter_2.html

## Slide 69: Active Filters

## Slide 70: End Unit 2
System Analysis