## Slide 1: Transfer Functions Mechanical Modeling
ME 357

## Slide 2: Objectives
By the end of this section, you should be able to
Create FBDs for linear and rotational mechanical systems (single- and multi-element)
Use FBDs to derive EOMs for system
Use EOMs to create transfer functions for I/O forces/displacements for SMD systems
Use Mathematica to assist with algebraic steps in deriving TF
Use Matlab to simulate step- and impulse inputs into TF

## Slide 3: Mechanical Element Modeling
Create ODEs from Newton’s Law
  Linear
  Rotational
  Pay attention to the coordinate system
Elements
  Spring
  Damper
Consider relative displacement of ends of springs and relative velocity of ends of dampers

## Slide 4: Transfer Function (TF)
TF is ratio of output to input when initial conditions are all zero
Always write in descending powers of
Derive algebraically first, then apply numerical values
Property of system, independent of input
For given TF, system response under different inputs can be studied and predicted
Determined experimentally by using known input and measuring output
In time domain, we will use state-space model
Used in next unit to predict behavior of system under different inputs
Notes: This is different than what we looked at before. The TF exists independent of the input
We always use this starting from rest. Can be modified for non-zero ICs

## Slide 5: Numeric Solutions
Once we have TF, it can be deployed in Matlab using
G = tf([num],[den])
  Where num is vector of coefficients in front of descending powers of in TF numerator
  Where den is vector of coefficients in front of descending powers of in TF denominator
Numerically solve for output (e.g., ) for basic inputs
  step(F*G); applies step of units as input
  impulse(F*G); applies impulse () of units as input
Can use IVT and FVT to determine starting value and steady-state value
Notes: You must account for coefficients of zero in the tf

## Slide 6: Example 1A
Consider the mechanical system shown. The system is initially at rest. The displacement x is measured from the equilibrium position. Assuming that is a force input and the displacement is the output, [1] obtain the algebraic transfer function of the system. Then, [2] applying kg, N-s/m, N/m and is a step force of magnitude 10 N (i.e., ), plot numeric solution (in Matlab) for . Verify with IVT and FVT.

## Slide 7: Example 1A
Notes: FVT predicts 10/6
IVT predicts 0 = 10/inf

## Slide 8: Multi-DOF Systems
System may have multiple DOFs due to multiple masses, nodes or ability of one mass to move in multiple directions
Create EOM for each DOF, usually making FBD for each
  Take Laplace Transform of each
Identify one output you need for desired TF
  Need to eliminate other output variables
Use algebraic substitution to solve for the TF
  May want to use Mathematica to assist for complicated systems
  There cannot be any dependent variables on the RHS

## Slide 9: Example 1B
Consider the mechanical system shown. The system is initially at rest. The displacements and are measured from their respective equilibrium positions. Assuming that is force input and the displacement is output, [1] obtain transfer function of system. Then, letting , , , , and is step force of magnitude 10N, [2] plot numeric solution for . [3] Compare to impulse input of 10 N-s.

## Slide 10: Example 1B Mathematica Steps
https://youtu.be/79m5Qg2sLsA

## Slide 11: Example 1B Matlab Results
Step Input of 10 N
Impulse Input of 10 N-s

## Slide 12: Example 2
The ﬁgure illustrates a simpliﬁed model of a vehicle suspension system. The system is originally at rest. The vehicle of mass is attached to an element that is modeled as a spring of stiffness in parallel with a viscous damper of damping coefficient . This element is in series with an element that is modeled as a spring of stiffness . The other end of this spring is subject to a time-dependent displacement, , caused by the terrain over which the vehicle is traveling. Determine the transfer function from input to output .

## Slide 13: Example 3
In the mechanical system, one end of the lever is connected to a spring and a damper, and a force is applied to the other end of the lever. Derive the transfer function for the output of to the input of . Assume that the displacement is small and the lever is rigid, intertialess and massless. The system is originally at rest.

## Slide 14: Example 4
Obtain transfer functions and for system shown. The vertical displacement, (at point ) is the input. This system is a simplified version of an automobile or motorcycle suspension system. and represent wheel mass and tire stiffness, respectively. Assume that displacements and are measured from their respective equilibrium positions in absence of input . The system is originally at rest.

## Slide 15: Example 4 Mathematica Steps
https://youtu.be/3zq0Tf67ByQ

## Slide 16: Example 5
A gear reduction system is used to increase angular velocity from an input motor as illustrated below. The angular velocity of output rotor is . Rotors are mounted on identical shafts, each of which has torsional viscous damping coefﬁcient . There is no slipping between gears. Input shaft is subject to torque . Derive transfer function from T to using only given parameters. Use for these externally-meshed gears. The system is originally at rest.
Notes: Use knowledge from 380
Signs depend on definition of positive axes
Rotor 2 will (generally) turn opposite the torque direction

## Slide 17: Example 6
Consider the spring-loaded inverted pendulum. Assume that the spring force acting on the pendulum is zero when the pendulum is vertical. Assume that the friction involved is negligible. Obtain a mathematical model of the system when the angle is small. Also, obtain the natural frequency of the system.

## Slide 18: Example
Obtain the transfer function of the system shown, whereis the force input. The displacement is measured from the equilibrium position.