## Slide 1: Electrical System Modeling (LRC)
ME 357

## Slide 2: Objectives
By the end of this section, you should be able to
Create transfer functions for input/output voltages/currents for LRC circuits
  Use current loops, voltage drops and voltage dividers
Use impendences to assist in deriving TFs
Understand how ideal op-amps work in LRC circuits
Continue to use Mathematica to work through algebraic problems to create TFs

## Slide 3: Electrical Modeling
Unlike mechanical systems, modeling will begin in frequency domain
  Ultimately want to make transfer function
Dependent variables of frequency will be voltages and currents
  Keep this in mind when making TF, no dependent variables on RHS

## Slide 4: Voltage Drop Across Electrical Components
Resistor
Capacitor
Inductor
Notes: Use “e” instead of “v” to not confuse with velocity

## Slide 5: Kirchhoff’s Laws
Voltage Law (KVL)
For any closed loop in circuit
Starting and ending at same node
  Add/subtract voltage from sources as appropriate
  Subtract voltage drops across elements
    Pay attention to total current through element
    Subtract when going with current; add going against
Can use multiple current loops
Notes: The sum of voltage gains/drops in a loop must be zero

## Slide 6: Kirchhoff’s Laws
Current Law (KCL)
For any node
Add current going into node and subtract current exiting
Notes: Total current entering node must equal total leaving: cannot “store” current at a node

## Slide 7: Additional Electrical Laws
Voltage drop between two nodes equal regardless of path between
Resistors in series:
Resistors in parallel:
Voltage Divider Law

## Slide 8: Voltage Source
When the current travels from negative to positive, add the voltage (electric potential)
When traveling positive to negative, subtract
Terminals also represented as: (same polarity as above picture)
Notes: Add or subtract based on assumed direction of current

## Slide 9: Simple Single-Loop R Circuit
Find current in circuit as function of voltage sources (not TF since it has multiple inputs)

## Slide 10: Multi-Loop R Circuit
Find currents in circuit as function of voltage sources (not TF since it has multiple inputs)

## Slide 11: RL Circuit
Find transfer function, . The switch is open until .
Notes: Open switch ensures zero ICs

## Slide 12: Single-loop RLC Circuit
Find transfer function, . The system has no input voltage for a long time before .
Notes: Starts with zero IC

## Slide 13: Multi-Loop RLC Circuit
Find transfer function, . The system has no input voltage for a long time before

## Slide 14: Impedance
To simplify circuits, can combine elements to find total impedance
Notes: Uses same parallel / series rules as resistors

## Slide 15: RLC Circuit using Impedance
Find transfer function . The system has no input voltage for a long time before

## Slide 16: Operational Amplifiers (OP-AMPS)
Takes input signal and outputs amplified (or attenuated) version of it
Can be inverting or non-inverting
  May reverse the polarity of signal
May introduce lag into signal
Typically are powered devices
Used in active filters (e.g., Butterworth)
Notes: We will ignore the external power requirements in the wiring diagram

## Slide 17: Ideal OP-AMPS
Assumptions
Input current is zero
Difference in input voltage is zero i.e.,

## Slide 18: Nodal Analysis
Label voltages at nodes that you can identify
  Voltages at inputs of op-amps equal
  Voltage at ground is zero
Label currents through wire
Voltage drop across element (voltage at current entrance minus exit) is product of current and impendence
Use voltage divider
Notes: Entrance minus exit gives positive value of voltage

## Slide 19: OP-Amp Example 1
Find transfer function . System has no input voltage for a long time before
Is circuit inverting or non-inverting?
Inverting circuit
Notes: Inverting circuits reverse the polarity of input signal

## Slide 20: OP-Amp Example 2
Find transfer function . System has no input voltage for a long time before
Is circuit inverting or non-inverting?
Inverting circuit

## Slide 21: OP-Amp Example 3
Find transfer function . System has no input voltage for a long time before
Is circuit inverting or non-inverting?
Non-inverting circuit