## Slide 1: 2nd-Order System Response
ME 357

## Slide 2: Objectives
By the end of this section, you should be able to
Put 2nd-order systems into standard form
Identify defining parameters of system
  Classify stability of system in TF or SS form
Sketch response of system due to step input
  Modify sketch when extra poles or zeros are added

## Slide 3: 2nd-Order Systems
General form for a 2nd-order system
When the input is a step function of magnitude
Roots of characteristic equation
General homogeneous solution
Notes: Oscillation depends on roots – value of zeta

## Slide 4: 2nd-Order Systems
Interested in predicting response of 2nd-order system (e.g. LRC circuit, or SMD) due to step function
Can implement passive control by tuning components in system (e.g. springs, masses, capacitors) to make system behave in desired way
Place transfer function into standard form for 2nd-order system
Notes: This form appropriate when there are no zeros

## Slide 5: 2nd-Order Systems Time Domain Response
where
is natural frequency.
is damping ratio.
is damped frequency (if underdamped system)

## Slide 6: 2nd-Order Systems Time Domain Response
Under-damped, oscillation around SS value
Critically-damped, no oscillation around SS
Over-damped, no oscillation around SS, slower convergence than critically damped
Notes: Step input response

## Slide 7: 2nd-Order Systems Time Domain Response
Complex poles
Real, repeated poles
Real, distinct poles
Purely imaginary roots: neutral stability
Poles in right half plane: unstable

## Slide 8: Typical Responses Step Input

## Slide 9: Typical Responses Step Input

## Slide 10: Pole Location Response

## Slide 11: Key Features of Under-Damped Systems
Rising time
Peak time
Overshoot
Settling time

## Slide 12: Rising Time
Time to increase/decrease from 10% to 90% of steady-state value
Notes: Not used often in this course

## Slide 13: Peak Time
Time from start to maximum value
Notes: This is half a period of oscillation

## Slide 14: Maximum Overshoot
Relative difference in maximum value and steady-state value ( is percent difference)
Notes: This is *not* the maximum value itself

## Slide 15: Settling Time
Time to be bound within (100X)% of SS value

## Slide 16: Example 1
Find dynamic response of system including: tR, tP, MP, tS,5%, yss and sketch the response

## Slide 17: Example 1

## Slide 18: Attenuation
Stable, under-damped systems oscillate around SS value, gradually losing energy
  Bound of oscillations has exponential decay
Frequency of oscillation not natural frequency, but rather damped frequency

## Slide 19: Frequency of Response Damped system
Damped system oscillates with angular frequency,
Find period of response using
Peak every seconds
Trough every seconds

## Slide 20: Attenuation of Response Damped system
Oscillations in stable, under-damped system attenuate over time
Oscillations bound above and below by
Find ratio of peak values (from peak to peak) using

## Slide 21: Example 2
Assume 2nd-order system with
Sketch response with proper attenuation and frequency

## Slide 22: Example 2

## Slide 23: Example 2

## Slide 24: State Space and 2nd-Order Response
ME 357

## Slide 25: State Space
Recall from state space model
Converting to transfer function
Thus, eigenvalues of A are poles TF
  Demonstrate same stability properties
Notes: With hand waiving:
sI-A is the “denominator” of the TF, thus its roots are the poles of the TF.

## Slide 26: State Space
From transfer function
Therefore, if eigenvalues/poles are in LHP and complex
Notes: There will not be an imaginary part if \zeta>=1

## Slide 27: Example 3
N
Create state-space model and find eigenvalues of A matrix
Put into TF form
  compare poles of system to previous results
  find response of

## Slide 28: Example 3

## Slide 29: Extra Poles and Zeroes 2nd-Order Systems
ME 357

## Slide 30: 1st-Order Review
Zero changed 1st-order system from standard form
System has initial value of
Steady-state value
How are 2nd-order systems impacted by additional zeroes and poles?

## Slide 31: Adding Poles and Zeroes
Compared to standard under-damped 2nd-order response, in general, adding:
Pole in LHP increases rising time and decreases overshoot significantly if extra pole is within four times real part of dominant poles
Pole in RHP will make system unstable
Zero in LHP increases overshoot and decreases rise time if zero is within four times real part of dominant poles
Zero in RHP depresses overshoot, but introduces initial undershoot
Zero in LHP “close” to extra pole may cancel effect of pole
Notes: Dominant poles are the complex conjugate pair from “base system”
Looking at qualitative changes

## Slide 32: Adding Poles and Zeroes
In short:
Pole in LHP decreases overshoot and increases rising time, especially within 4 times real part of dominant pole
  Add as:
Zero in LHP increases overshoot and decreases rising time, especially within 4 times real part of dominant pole
  Add as:

## Slide 33: How are Poles and Zeros Added to System?
Instead of having open-loop systems, will be adding feedback control in next unit
Modify system response with specified input
  Can add zeroes using derivatives of signals
  Can add poles using integrals of signals

## Slide 34: Analysis Method
Find dominant poles of underdamped system
  These are complex conjugate pair
Find “extra” pole or zero
  This will be real
  Factor out of denominator in form of and numerator in form of
“Baseline” system is one where you ignore “extra” term(s)
  Estimated response is then based on extra term(s)
  Making qualitative assessment, not quantitative, in this course
Notes: May find poles numerically

## Slide 35: Additional LHP Pole
Notes: Will show factoring only in first example

## Slide 36: Additional LHP Zero

## Slide 37: Additional RHP Zero

## Slide 38: Additional Zero close to Additional Pole