## Slide 1: Feedback Control
ME 357

## Slide 2: Objectives
By the end of this section, you should be able to understand
The general concept of feedback control
How using amplification of error as input into a system can change its behavior (P Controller)
How using amplification of the sum of the error as input into a system can change its behavior (I Controller)
The success of a controller is dependent on the “plant” and the desired response

## Slide 3: Feedback Control
Previously looked at passive control
  e.g., changing spring constants or resisters to change response behavior
Now look at active control
  Prescribing input function to system to achieve desired output response
  Use output(s)/observable(s) to determine input(s) into system
In Unit 2, given input into system (step or sinusoidal) found output response
  This section we do opposite: have desired output response and determine system input to “best” achieve it
Consider only step outputs in this course

## Slide 4: Intro Example
Use ,
Initially, voltage across capacitor, , is 0 VDC, we want it to be constant 5 VDC once time begins. What should input voltage, , be to accomplish this?
Notes: Looking for SS output of 5 VDC. Ideally, it would get there instantly

## Slide 5: Intro Example
Use step input of 5 VDC for Ei (Open Loop)
Ramp input to 5 VDC for Ei (Open Loop)
Change Ei dynamically based on the value of Eo (Closed Loop)
Notes: These are only three examples, there are infinite number of inputs that would provide desired SS output

## Slide 6: Comparison (1 & 2)
Step Input
Ramp Input
Notes: notice the different input profiles produce different output profiles

## Slide 7: Closing the Loop
G0(s)
+-
K
R
G0(s)
Eo
Ei
Open-Loop System
Closed-Loop System
Notes: Reference is how we want output to look
Error is difference between current value and our desire
Error is zero when they match

## Slide 8: General Feedback Controller Schematic
Notes: For this course, we typically ignore (set to “1”) actuator and sensor. These will have their own TFs that affect response of system

## Slide 9: Proportional (P) Control
G0(s)
+-
K
R
Eo
R-Eo=err
K err = Ei
Notes: SS value / Error is dependent on gain
Note that system’s TF is now different than plant
G0= Eo/Ei will be referred to as OL system or plant
Eo/R is CL system or feedback system

## Slide 10: Proportional (P) Control Simulink Schematic

## Slide 11: KP=1

## Slide 12: KP=2

## Slide 13: KP=10

## Slide 14: Comparison
Notes: The output voltage increases as the gain increases

## Slide 15: Proportional (P) Control
Proportional controller cannot drive error to zero for this plant
  Not universally the case
Steady-state error can be driven toward zero asymptotically, but requires very high gain
  High gain causes high peak input voltage into system
Need more than just proportion of error to drive input in this system
Notes: Success of controller depends on the open-loop TF (i.e., plant)

## Slide 16: Integral (I) Control
Instead (or in addition) to driving error itself to zero, can drive summation (integral) of error to zero
  Area under error curve
  Positive and negative values will cancel out over time
  Error itself will have to go to zero for its integral to go to zero
Will change the order of CL system
Notes: This is another possible controller choice

## Slide 17: Integral (I) Control
G0(s)
+-
KI
R
Eo
R-Eo=err
KI/s err = Ei
1/s
Notes: OL system is 1st-order, CL system is 2nd-order with I controller
The steady-state output is now always 5 regardless of gain

## Slide 18: Integral (I) Control
G0(s)
+-
KI
R
Eo
R-Eo=err
KI/s err = Ei
1/s
Notes: CL TF is 2nd order
choice of gain effects natural frequency and damping ratio. Thus, it effects peak time and max overshoot

## Slide 19: Integral (I) Control

## Slide 20: KI=1

## Slide 21: KI=5

## Slide 22: KI=25

## Slide 23: KI=0.1: Critically Damped

## Slide 24: Comparison

## Slide 25: Integral (I) Control
Integral controller drives error to zero for this system regardless of gain
  Not universally true
Increasing gain (and thus maximum input voltage) drives system to steady state differently
  Different damped frequency, overshoot, etc.
  Eventually reaches SS regardless of chosen gain
Closed-loop system is open-loop system with additional pole (and gain)
  Effectively increases order of this system to 2nd-order
  Introduces oscillations and overshoot despite having 1st-order plant (OL system)